## Slide 1
Local Network System
For Sharing School
A Complete Internet-Independent Educational Network
GNS3
Cisco IOS
Ubuntu 24.04
Moodle LMS
VLAN
ACL
Computer Networks Project • 2025–2026

## Slide 2
Presentation Overview
01
Project Overview
Goals, motivation, and problem statement
02
Network Topology
Architecture, VLANs, and device layout
03
Router & Switch Config
Inter-VLAN routing, DHCP, and ACL setup
04
Server Services
DNS, DHCP, Apache, Samba, FTP
05
Moodle LMS
E-learning platform on local network
06
Security — ACL
Network access control and isolation
07
Web Portals
Admin, Teacher, and Student interfaces
08
Results & Conclusion
Testing outcomes and key achievements

## Slide 3
01 — Overview
Project Overview
The Problem
Many schools lack reliable internet yet need digital tools for modern education.
Standard services — LMS, file sharing, DNS — require internet in most setups.
This creates a digital divide that disadvantages students in underconnected regions.
Our Solution
A complete, self-contained Local Area Network that delivers all essential digital educational services — entirely without internet.
4
VLANs
6+
Services
100%
No Internet
3
User Roles

## Slide 4
02 — Topology
Network Topology & VLAN Design
MainRouter
Cisco IOS — R1
MainSwitch (Core)
SW-Admin
VLAN 10
PC-Admin
192.168.10.0/24
SW-Teachers
VLAN 20
PC-Teachers
192.168.20.0/24
SW-Students
VLAN 30
PC-Students
192.168.30.0/24
SW-Servers
VLAN 40
DNS+Samba+Moodle
192.168.40.0/24
Trunk (dot1Q 802.1Q)

## Slide 5
03 — Configuration
Router — Inter-VLAN, DHCP & ACL
Router-on-a-Stick
Single physical interface (Fa0/0)
4 sub-interfaces — one per VLAN
dot1Q encapsulation per VLAN ID
Each sub-interface = gateway for its VLAN
DHCP Pools
ADMIN
192.168.10.x
TEACHERS
192.168.20.x
STUDENTS
192.168.30.x
ACL Security
BLOCK_STUDENTS
Applied on Fa0/0.30
DENY VLAN30→VLAN10
No Admin access
DENY VLAN30→VLAN20
No Teacher access
PERMIT any any
Servers OK
Key Cisco IOS Commands
R1(config)# interface FastEthernet0/0.10
R1(config-subif)# encapsulation dot1Q 10
R1(config-subif)# ip address 192.168.10.1 255.255.255.0
R1(config)# ip access-list extended BLOCK_STUDENTS
R1(config-ext-nacl)# deny ip 192.168.30.0 0.0.0.255 192.168.10.0 0.0.0.255

## Slide 6
04 — Services
Server Services
192.168.40.10
Primary Server — DNS-DHCP-WEB-Moodle
Apache
School intranet portal on port 80
BIND9
DNS server for school.local on port 53
ISC-DHCP
IP allocation for VLANs 10, 20, 30
Moodle
Full LMS on http://moodle.school.local
MySQL
Database backend for Moodle
192.168.40.20
Secondary Server — Samba-FTP
Samba
[Shared] [Teachers] [Students] shares
vsftpd
FTP server on port 21, anonymous access
Auth
Teacher-only share with password

## Slide 7
05 — Moodle LMS
Moodle 4.4 — Learning Management System
E-Learning Without Internet
Full Moodle 4.4 LMS running entirely on the local school network at moodle.school.local
Course Management
Create & manage courses, enroll students
Assignments
Upload homework, set deadlines, grade online
Quizzes & Exams
Build assessments with automatic grading
File Resources
Share PDFs, videos, documents within courses
Discussion Forums
Student-teacher interaction and peer learning
Grade Reports
Track student progress and performance
Stack: Apache + PHP 8.x + MySQL 8.0 + Moodle 4.4 (MOODLE_404_STABLE)

## Slide 8
06 — Security
Network Security — ACL Enforcement
ACL: BLOCK_STUDENTS
Applied: Fa0/0.30 — inbound direction
✕
DENY VLAN30 → VLAN10
Students cannot access Admin VLAN
✕
DENY VLAN30 → VLAN20
Students cannot access Teacher VLAN
✓
PERMIT any → any
All other traffic is allowed
Live Test Results
PC-Students
→ 192.168.10.1 (Admin)
✕
PC-Students
→ 192.168.20.1 (Teacher)
✕
PC-Students
→ 192.168.40.10 (Server)
✓
PC-Students
→ 192.168.30.1 (Own GW)
✓
PC-Teachers
→ All VLANs
✓
PC-Admin
→ All VLANs
✓
ACL Result:
Students are completely isolated from Admin and Teacher VLANs while retaining full access to Servers (Moodle + File sharing).

## Slide 9
07 — Web Portals
Role-Based Web Portals
Admin Portal
admin.html
🔑 admin / admin123
Full network dashboard
VLAN details & devices
ACL rules & results
File management
Service status panel
Links to all portals
Teacher Portal
teacher.html
🔑 teacher / teacher123
Upload files with metadata
Set subject & audience
My-files management
Upload progress bar
Moodle LMS button
Statistics panel
Student Portal
student.html
🔑 student / student123
Browse available files
Search & filter by subject
Download any file
Cannot upload files
Moodle LMS button
Auto-refresh every 10s
Unified login page (index.html) routes users to their portal based on credentials • Accessible at http://192.168.40.10

## Slide 10
08 — Results
Results & Conclusion
VLAN Segmentation
4 isolated VLANs — all devices separated correctly
Inter-VLAN Routing
All VLANs communicate via Router-on-a-Stick
DHCP Assignment
Correct IPs assigned in each VLAN automatically
DNS Resolution
school.local resolves internally — 0% internet
ACL Enforcement
Students blocked from Admin/Teacher VLANs — verified
Moodle LMS
Full e-learning platform running locally
Conclusion:
This project proves that a complete, internet-independent educational digital infrastructure — including an LMS — is achievable using open-source tools and standard networking hardware.

## Slide 11
Thank You!
Questions are welcome
Project:
Local Network System For Sharing School
Tools:
GNS3 + Cisco IOS + Ubuntu 24.04 + Moodle 4.4
Domain:
school.local — 100% Internet-Free